# File Format: .JTF
JTF stands for "JUMP TIN Format." It is a simple, efficient, geospatially aware standard file format for Triangular Irregular Networks (TINs). This format was initially designed to work with OpenJUMP/JTIN and allow for easy analysis and display.

# Motivation and History
JTF is inspired by the ITF format from vterrain.org (http://www.vterrain.org/implementation/Formats/ITF.html). The primary differences between JTF and ITF is the expansion of JTF to store connectedness between the triangles as well as breaklines and boundaries. These changes allow for quicker loading of TINs that are to be used for analysis rather than just display. JTF was proposed and implemented by Christopher DeMars in 2008 as part of the Google Summer of Code program.

# Current format spec: JTF Version 1.0
The file begins with a header, containing the following:

Field	Length in Bytes	Description
File_Marker	6	A marker which indicates that this is a JTF file. For version 1.0 of the format, it contains the characters "jtin01"
Num_Vertices	4 (int)	Number of vertices in the TIN.
Num_Triangles	4 (int)	Number of triangles that compose the TIN.
Num_Breaklines	4 (int)	Number of breaklines present.
Num_Boundaries	4 (int)	Number of boundaries present.
Data_Start	4 (int)	File offset where the data starts. A parser should seek to this position to read it
SRID	4 (int)	EPSG code representing the spatial ID for this TIN.

Next is the data itself, vertices, then triangles, then connections between the triangles, then breaklines, then finally boundaries.

Each vertex is encoded using the following format:

Field	Length	Description
X	8 (double)	X coordinate (easting)
Y	8 (double)	Y coordinate (northing)
Z	8 (double)	Z coordinate (elevation) Note: this differs from the ITF spec by using a double rather than a float in order to better fit the Java Topology Suite.

Next are the triangles, which each contain the array indices of their three vertices (index corresponds to the above array of vertices) and the indices of the three neighboring triangles (index corresponds to this array of triangles). Vertices should be listed in clockwise direction when viewed from above the surface. Neighboring triangles should be listed in clockwise ordering starting with the triangle opposite the point Vertex_Idx1:

(TODO: decide if triangles on a border should have the neighbor entry on the border edge set at -1 or linked to the next edge along the breakline that shares one of this triangle's vertices. I'm leaning to linking to the neighbor as this would make some algorithms easier.)

Field	Length	Description
Vertex_Idx1	4 (int)	First corner.
Vertex_Idx2	4 (int)	Second corner.
Vertex_Idx3	4 (int)	Third corner.
Triangle_Idx1	4 (int)	Index of neighboring triangle opposite Vertex_Idx1
Triangle_Idx2	4 (int)	Index of neighboring triangle opposite Vertex_Idx2
Triangle_Idx3	4 (int)	Index of neighboring triangle opposite Vertex_Idx3

Next is a list of breaklines. Each breakline entry begins with the number of vertices composing the breakline followed by that many indices to the vertex table. Vertexes should be listed in order. If the breakline forms a ring, the first and last vertex indices should be equal.

This data section is optional and may not be included for a given TIN. In that case Num_Breaklines in the header will be equal to zero.

Field	Length	Description
Breakline_Length	4 (int)	Number of points composing the breakline.
Vertex_Idx1	4 (int)	First vertex of the breakline.
...	...	...
Vertex_IdxN	4 (int)	Last vertex: N = Breakline_Length

The final data section is a list of boundary lines. They follow the same format as the Breakline table above.

Field	Length	Description
Boundary_Length	4 (int)	Number of points composing the boundary.
Vertex_Idx1	4 (int)	First vertex of the boundary.
...	...	...
Vertex_IdxN	4 (int)	Last vertex: N = Boundary_Length

# Notes

# Code